## Slide 1
CRU
Coordinate Rotation Unit
CORDIC-Based Trigonometric Co-Processor for StarCore-1
OrbitEdge-1 Mission · Attitude Determination Subsystem
18 cycles
Bounded Latency
6×
Speedup vs SW
0
Multipliers
16/16
Tests Pass
Emmanuel Basua · Adedamola Yusuff · Sanjan Naidoo
EEE4120F HPES Project | Milestone 2 Demo | 2026

## Slide 2
The Problem
Why does a satellite processor need a dedicated trig co-processor?
🔢
Attitude Determination
StarCore-1 must compute sin θ and cos θ on every control-loop iteration for quaternion-based satellite orientation. Trig is the dominant workload.
🐌
Software Cost
A software CORDIC loop on StarCore-1 takes ~108 instruction cycles per sin/cos pair — too slow for real-time attitude control at mission frequency.
📦
No FPU, No LUT
Radiation-tolerant FPGAs cannot afford a floating-point unit or a large lookup table. The CRU uses only shift-and-add arithmetic in 18 cycles.
Solution: Offload trig to dedicated CORDIC hardware — 6× speedup, zero multipliers, bounded 18-cycle latency

## Slide 3
System Architecture
CRU hangs off the StarCore-1 reserved opcode 1010 slot via a custom co-processor bus
StarCore-1
CPU Core
· 16-bit RISC
· Harvard architecture
· Single-cycle execution
· Opcode 1010 reserved
for co-processor
CRU
Co-Processor
· CORDIC FSM (3 states)
· 16 shift-and-add iterations
· 16-entry atan ROM
· Q1.15 fixed-point output
· 18-cycle bounded latency
START, ANGLE_IN →
← BUSY, VALID
← COS_OUT, SIN_OUT
Opcode 1010 | Custom Co-Processor Bus
MMIO / Memory Bus

## Slide 4
CORDIC Engine Design
Rotation mode — iterative shift-and-add, no multipliers required
Algorithm
Update equations (per iteration): xi+1 = xi − d·yi·2−i
y
i+1 = yi + d·xi·2−i
z
i+1 = zi − d·atan(2−i) d = sgn(z) — direction bit 2−i = arithmetic right-shift (free in hardware) Initial values: x₀ = K⁻¹ = 0x4DB8 (0.6072 in Q1.15) y₀ = 0 z₀ = θ (Q0.14 normalised) After 16 iterations: x→cos θ, y→sin θ
Moore FSM — 3 States
IDLE
BUSY=0 VALID=0
ITER
BUSY=1 VALID=0
DONE
BUSY=0 VALID=1
START=1
load x₀,y₀,z₀
i=16
latch result
i<16
CORDIC step,
i←i+1
START = 0
18-cycle bounded latency (1 load + 16 iter + 1 done)

## Slide 5
Gold Standard — What Is It?
The reference we compare all hardware results against
The Concept
A gold standard (or golden measure) is a trusted reference output computed by a high-precision tool, used to verify that your hardware produces correct results. Our gold standard: Python math.cos() / math.sin() IEEE 754 double precision (64-bit) Accurate to 15 decimal places The CRU uses 16-bit fixed-point Q1.15 (max 15 fractional bits of precision). We quantise the Python result to Q1.15 then compare — any difference is the CORDIC quantisation error in LSBs.
Verification Flow
Input
theta = 0x400
(= 45 degrees)
↓
Gold Standard
Python: cos(45°) = 0.70711
Quantised to Q1.15: 0x5A82
↓
CRU Hardware
CORDIC 16 iterations
Output: 0x5A7E
↓
Compare
|0x5A7E − 0x5A82| = 4 LSB
4 ≤ 20 threshold → PASS

## Slide 6
Gold Standard Results
CRU Q1.15 output vs IEEE double-precision reference — 16 angles tested
Angle | θ (hex) | cos (IEEE float) | sin (IEEE float) | CRU cos | CRU sin | Err (LSB)
0° | 0x000 | 1.00000 | 0.00000 | 0x7FFD | 0x0002 | ≤3
15° | 0x155 | 0.96593 | 0.25882 | 0x7BA3 | 0x211C | ≤5
30° | 0x2AB | 0.86603 | 0.50000 | 0x6ED4 | 0x4005 | ≤6
45° | 0x400 | 0.70711 | 0.70711 | 0x5A7E | 0x5A81 | ≤4
60° | 0x555 | 0.50000 | 0.86603 | 0x4005 | 0x6ED4 | ≤6
75° | 0x6AB | 0.25882 | 0.96593 | 0x2114 | 0x7BA5 | ≤13
-45° | 0xC00 | 0.70711 | -0.70711 | 0x5A84 | 0xA582 | ≤4
-75° | 0x955 | 0.25882 | -0.96593 | 0x211F | 0x845D | ≤3
All 16 tests PASS · Max error 20 LSB = 0.061% of full scale · Threshold set to 20 LSB (theoretical limit for 16-iteration CORDIC)

## Slide 7
Simulation Results
iVerilog + VCD — 16-angle sweep — all tests self-checking
Terminal Output
============================================== CRU Simulation cordic_engine.v ============================================== [PASS] Test 0 | θ=0x000 | cos=0x7ffd(err=0) sin=0x0002(err=0) | cyc=17 [PASS] Test 1 | θ=0x0e4 | cos=0x7e08(err=0) sin=0x1648(err=0) | cyc=17 [PASS] Test 2 | θ=0x155 | cos=0x7ba3(err=0) sin=0x211c(err=0) | cyc=17 [PASS] Test 3 | θ=0x200 | cos=0x763c(err=11) sin=0x30fd(err=1)| cyc=17 ... (tests 4–14 all PASS) ... [PASS] Test 15 | θ=0x000 | cos=0x7ffd(err=0) sin=0x0002(err=0) | cyc=17 ============================================== PASS: 16 FAIL: 0 TOTAL: 16 *** ALL TESTS PASSED *** ==============================================
16/16
Tests Passed
17
Cycles to VALID
(after START)
≤20
Max Error
(LSB)
0
Failures or
Timeouts

## Slide 8
Performance Analysis
CRU vs StarCore-1 software CORDIC — Amdahl's Law framing
Amdahl's Law
Speedup = 1 / (1-p + p/s)
SW
108 cy
CRU
18 cy
6x
trig speedup
~3.2x
overall (Amdahl)
Metric | SW CORDIC | CRU
Cycles / sin+cos | ~108 | 18
Multiplier needed | Yes | No
LUT table size | Large | 16 entries
Latency bounded? | No | Yes — 18 cy
Speedup (trig op) | 1× | 6×
Overall speedup* | 1× | ~3.2×
Area (est.) | Shared | ~200 LUTs
* Amdahl's Law: if trig = 83% of runtime, overall speedup = 1/(0.17 + 0.83/6) ≈ 3.2× — the remaining 17% limits total gain

## Slide 9
Key Takeaways
⚡ 6× Speedup
CRU computes sin/cos in 18 cycles vs ~108 cycles for software CORDIC on StarCore-1
✅ Verified Accuracy
16/16 gold standard tests pass — worst case 20 LSB = 0.061% error vs IEEE double-precision
🔧 Multiplier-Free
Purely shift-and-add CORDIC — no DSP blocks, ideal for radiation-tolerant FPGA
🔗 Clean Interface
Opcode 1010 co-processor bus, BUSY/VALID handshake, bounded latency — zero pipeline stalls
OrbitEdge-1 · CRU Co-Processor · EEE4120F HPES 2026